## Slide 1
Performance of the LHCb VELO
Outline
LHCb Detector and its performance in Run I
LHCb VELO
VELO performance in Run I and radiation damage
Look into the future – Run II and upgrade
Summary
On behalf of the LHCb Collaboration
Tomasz Szumlak AGH-UST
Jagiellonian Symposium of Fundamental and Applied Subatomic Physics
07/06 – 12/06/2016, Krakow, Poland

## Slide 3
LHCb is dedicated for studying heavy quark flavour physics
It is a single arm forward spectrometer with pseudorapidity coverage 2 < η < 5
Precise tracking system (VELO, upstream and downstream tracking stations and 4 Tm magnet)
Particle identification system (RICH detectors, calorimeters and muon stations)
Partial information from calorimeters and muon system contribute to L0 trigger (hardware)
that works at LHC clock – 40 MHz
Max rate of full detector readout at 1.1 MHz
The LHCb detector at LHC (JINST 3 2008 S08005)

## Slide 4
Summary of the LHCb Performance

## Slide 5
Operation conditions of the LHCb in 2011
  recorded luminosity L ≈ 1,2 [fb-1] at beam energy 3.5 [TeV]
  LHCb stably operated at Linst = 4.0 x 1032 [cm-2s-1 ] (nominal 2.0 x 1032)
  Average number of visible interactions per x-ing µ = 1.4 (nominal 0.4)
  Data taking efficiency ~90 % with 99 % of operational channels
  HLT (High Level Trigger) input ~ 0.85 MHz, output ~ 3 kHz
  Ageing of the sub-detectors monitored – according to expectations
Luminosity leveling
Use displaced p-p beams
Lower inst. Luminosity
Stable conditions during the run
Lower pile-up

## Slide 6
Operation conditions of the LHCb in 2012
  Beam energy 4.0 [TeV] (15 % increase of the b-barb x-section)
  Keep the luminosity at Linst = 4.0 x 1032 [cm-2s-1 ] for this year
  Average number of visible interactions per x-ing slightly higher µ = 1.6
  Keep high data taking efficiency and quality
  HLT (High Level Trigger) input ~ 1.0 MHz, output ~ 5 kHz (upgraded HLT farm and revisited code)
  Collected ~ 2.1 fb-1 of collision data

## Slide 7
Intriguing results from LHCb – possible hints of New Physics
No NP effects has been confirmed so far, however…
Two interesting anomalies seen by LHCb
observable measured in the above the SM predictions
Rates of charged beauty semileptonic decays below the SM predictions

## Slide 8
Overall summary of Run I
LHCb:
  Superb performance – greatly exceeded any expectations
  Stable operation at inst. luminosity 100% higher than nominal
  General purpose detector in forward direction
  Many world best results
  Over 230 papers published!
The pinch of salt:
  No conclusive BSM physics discovered
  There is still room for NP!
  Need push precision to the limits in order to challenge theoretical predictions
  Need more data

## Slide 9
Data taking road map for LHCb before the upgrade

## Slide 10
The LHCb VELO (VErtex LOcator)
VELO surrounds the proton-proton interaction point
Consists of two halves that can be open and close
  They are retracted (30 mm) during beam injection and closed (5 mm) for the collisions

## Slide 11
The LHCb VELO (VErtex LOcator)
21 stations per half, each of which has one R- and -type sensors
Two pile-up stations in each half (trigger)
First active channel just 8.2 mm from the proton beam
Operates in secondary vacuum separated from the beam vacuum by 300 µm thick foil
CO2 cooling system

## Slide 12
VELO sensors
Semicircular micro-strip silicon sensors with floating pitch (40 – 100 µm)
One R- and one -type sensor per module
300 µm thick
Signal routed via second metal layer
2048 strips (channels) per sensor
  Two 45 degree quadrants for R-type
  Two regions of short and long strips
~ 180 000 readout channels in total!

## Slide 13
Signal and noise
-sensor
Typical noise measured to be around 2 ADC (Analog to Digital Count) counts
ADC distribution fitted with Landau convoluted with Gaussian (MPV for signal/noise)
Signal to noise performance
-sensor
-sensor

## Slide 14
Resolutions
Single hit resolution
IP resolution
PV resolution
Excellent single hit resolution ~ 4 µm for the optimal angle and smallest sensor pitch
Primary Vertex resolutions: and for 25 tracks
Impact Parameter:
Very good agreement between data and simulation
  Performance of the LHCb VELO (JINST 9 2014 P09007)

## Slide 15
Radiation Damage
Harsh hadronic environment – particle fluences up to
Charged particle flux causes surface and bulk damage and has direct impact on
  Leakage current
  Effective doping concentration
This must be carefully monitored and analysed
  Currents vs. Voltage (a.k.a. IV scan)
  Currents vs. Temperature (a.k.a. IT scan)
  Full Depletion Voltage
  Cluster Finding Efficiency

## Slide 16
Leakage currents
Measured leakage current in good agreement with predicted values
  Typical increase
  Dominated by the bulk current
Observed increase in current proportional to the fluence
All sensors (Run I) operated at the nominal bias voltage 150 V and temperature of -7
All effects well understood!

## Slide 17
Radiation damage monitoring – Effective Depletion Voltage (EDV)
Measured during assembly – capacitance at different bias voltages – not possible during operation!
Method based on track extrapolation to test sensor, which bias voltage is varied (0 – 150 V)
EDV is the voltage at which the MPV is ~ 80% of the plateau

## Slide 18
Radiation damage monitoring – Effective Depletion Voltage (EDV)
  Effective depletion voltage decrease with fluence
  Minimum of observed @ ~
  Overall good agreement with the Hamburg Model for both low and high fluences – the apparent departure related to small electric field
  Can operate the current VELO till the end of Run II

## Slide 19
  Fully operational VELO replacement has been built in case of an accident with beam
  Need to define new procedures for CCE
  More aggressive approach to calibration scans – done on daily basis
  is not going to be uniform across sensors – careful monitoring needed
  Operation with different bias voltage for different sensors envisaged
Preparation for Run II (started officialy last week)

## Slide 20
Why upgrade (i.e., what’s wrong with the current design…?)
Superb performance – but 1 MHz readout is a sever limit
can collect ~ 2 fb-1 per year, ~ 5 fb-1 for the „phase 1” of the experiment
this is not enough if we want to move from precision exp to discovery exp
cannot gain with increased luminosity – trigger yield for hadronic events saturates
Upgrade plans for LHCb do not depend on the LHC machine
we use fraction of the luminosity at the moment
Upgrade target
full event read-out@40 MHz (flexible approach)
completely new front-end electronics needed (on-chip zero-suppression)
redesign DAQ system
HLT output@20 kHz, more than 50 fb-1 of data for the „phase 2”
increase the yield of events (up to 10x for hadronic channels)
experimental sensitivities close or better than the theoretical ones
expand physics scope to: lepton flavour sector, electroweak physics, exotic searches and QCD
Installation ~ 2018 - 2019
Preparation for Run II (started officialy last week)

## Slide 21
VErtex LOcator VELO2
Current design: R-Φ geometry Si strip sensors with pitch between 38 – 100 µm
To be replaced with pixel based device
  low occupancy
  much easier patter recognition
  easier to control alignment
  radiation hardness
  extremely high data rate ~ 12 Gbit/s
  un-uniform data rates/radiation damage
  micro-channel CO2 cooling
Read-out ASIC, VeloPix, based on TimePix/Medipix chip
  256x256 pixel matrix
  equal spatial resolution in both directions
  IBM 130 nm CMOS process
  great radiation hardness potential ~ 500 Mrad

## Slide 22
VErtex LOcator VELO2
Predicted performance superior in almost any aspect w.r.t the current VELO
This is essential for physics performance of the upgraded spectrometer
(VELO Upgrade: Technical Design Report, LHCb-TDR-13)

## Slide 23
SUMMARY
  Excellent performance of the LHCb VELO during Run I data taking
    Average signal to noise: and
    Single hit resolution ~ 4 µm
    Typical IP resolution ~ 12 µm for high perpendicular momentum
    Typical PV resolution ~ 13 (69) µm in x, y (z) for 25 tracks
  Radiation damage effects studied and understood
    Leakage currents (bulk dominated) increase ~
    Type inversion observed in inner part of sensors
    Increase of EDV
  Major upgrade of the LHCb VELO detector is planned
    New readout electronics and sensors (pixels)

## Slide 24
Back-up

## Slide 25
What we must change to cope with the 40 MHz read-out
VELO
Si strips
(replace all)
Silicon Tracker
Si strips
(replace all)
Outer Tracker
Straw tubes
(replace R/O)
RICH
HPDs
(replace HPD & R/O)
Calo
PMTs (reduce PMT gain, replace R/O)
Muon MWPC
(almost compatible)

## Slide 26
Run II and the upgrade road map
Summary

## Slide 27
Vertex Locator
Dipole magnet
TT+IT (Silicon Tracker)
Calorimeters
Muon system
RICH detectors
300(H)/250(V) mrad
15mrad
OT
Interaction
Point
OT – Outer Tracker
IT – Inner Tracker
TT – Trigger Tracker
Single arm spectrometer geometry
Fully instrumented in rapidity range 2 < η <5
Capable of reconstructing backward tracks (-4 < η < -1.5)